## Slide 1: Inexpensive Prosthetic Hand with EMG Control
Unique ID: SUP-021
Team Name: Tech NovaCorps

## Slide 2: Introduction
Developing an Inexpensive Prosthetic Hand
EMG Signal Acquisition from Flexor Carpi Ulnaris Muscle (FCU) or Ulnar Nerve
Utilizing Muscle BioAmp Candy from Upside Down Labs

## Slide 3: Technology Overview
Muscle BioAmp Candy
  Compact EMG Sensor
  Fixed Gain (x2420)
  Bandpass Filter (72 – 720Hz)
Arduino Nano Microcontroller
  Signal Processing
  Servo Controlling Using PWM Signals

## Slide 4: Components Used
Muscle BioAmp Candy
Arduino Nano Microcontroller
3D Printed Prosthetic Hand
Servo Motors(5)
Overall System Cost Breakdown
Component Name | Price in Rupees
Muscle BioAmp Candy | 700
Arduino Nano Microcontroller | 250
3D Printed Prosthetic Hand Components | 1500
Servo Motors(5) | 510
Total | 2960

## Slide 5: Cost Comparison
Market Alternatives Cost
  Range: 5,000 USD to 8,000 USD
  (415K-664K INR)
Project Cost
  Total: 3,000 rupees or 37 USD
  Emphasizing Cost-Effectiveness

## Slide 6: What is EMG?
The EMG signal is generated by the electrical activity of the muscle fibers active during a contraction.
The signal sources are the depolarizing and repolarizing zones of the muscle fibers.

## Slide 7: Muscle BioAmp Candy
Band-Pass Butterworth IIR digital filter(72-720Hz)
Sampling rate: 500.0 Hz,
Filter is order 4, implemented as second-order sections (biquads).

## Slide 8: Signal Processing
Role of Muscle BioAmp Candy
  Instrumentation Amplifier
  Non Inverting Amplifier
  Bandpass Filter (72 – 720Hz)
Role of Arduino Nano
  Works as ADC for converting the
  analog signals to digital signals
  Envelope Detection

## Slide 9: Conclusion
Economic Viability and Affordability
Bridging the Gap in Prosthetic Technology
Future Potential and Development

## Slide 10: References
https://docs.scipy.org/doc/scipy/reference/generated/scipy.signal.butter.html
https://courses.ideate.cmu.edu/16-223/f2020/Arduino/FilterDemos/filter_gen.py
https://github.com/upsidedownlabs

## Slide 11: Team Members
Rajdeep Saha (Electronics and Communication Engineering)
Abhijit Biswas (Electronics and Communication Engineering)
Saradwat Sen (Electronics and Communication Engineering)
Sayani Dhali (Electronics and Communication Engineering)